## Slide 1: Innovative/Alternative Septic System Performance
System Performance and Tracking it with the Carmody Database
Brian Baumgaertel, Environmental Project Assistant
Barnstable County Department of Health and Environment

## Slide 2: County I/A Program Overview
Started in 2005 under a grant from EPA.
Covers 14 towns of Barnstable County.
All operators of I/A systems report results of inspections and sampling events to a web-based database.
Provide initial level of compliance on behalf of town Boards of Health.
Now funded by a database user fee paid by operators based on the number of contracts they hold.

## Slide 3: Box-Whisker Diagrams
50%
Probability Density Graph (“Bell Curve”)
Median – Middle Value
Min/Max Value
Box
Whiskers
What are they?
Min/Max Value
25%
25%

## Slide 4: Box-Whisker Diagrams
What Can We Use Them For?
A
B
C
D
A – A “Good” System. Box and whiskers are short and compact.
B – A “Bad” System. Results are all over the place. Box and whiskers are stretched out.
C – A “Consistently Bad” System. Compact but well above TN limit (19 mg/l)
D – A “Usually Pretty Good” System. Compact but maybe a couple of high results.

## Slide 5: Single Family all Types by Individual System
Three or More Samples with Full Nitrogen Series
89 systems with 3 or more TN samples
58 (65%) with median TN <19 mg/l

## Slide 6
Single Family all Types by System Type
Three or More Samples with Full Nitrogen Series

## Slide 7: Single Family Advantex
Three or More Samples with Full Nitrogen Series
12 systems with 3 or more TN samples
10 (83%) with median TN <19 mg/l

## Slide 8: Single Family Bioclere
Three or More Samples with Full Nitrogen Series
7 systems with 3 or more TN samples
5 (71%) with median TN <19 mg/l

## Slide 9: Single Family FAST
Three or More Samples with Full Nitrogen Series
40 systems with 3 or more TN samples
28 (70%) with median TN <19 mg/l

## Slide 10
Single Family SeptiTech Pre-Reconfiguration
Three or More Samples with Full Nitrogen Series
18 systems with 3 or more TN samples
4 (22%) with median TN <19 mg/l

## Slide 11
Single Family SeptiTech Post-Reconfiguration
Three or More Samples with Full Nitrogen Series
16 systems with 3 or more TN samples
6 (38%) with median TN <19 mg/l

## Slide 12
Single Family Singulair
Three or More Samples with Full Nitrogen Series
4 systems with 3 or more TN samples
4 (100%) with median TN <19 mg/l

## Slide 13
Single Family Waterloo Biofilter
Three or More Samples with Full Nitrogen Series
6 systems with 3 or more TN samples
6 (100%) with median TN <19 mg/l

## Slide 14
Single Family Miscellaneous Other Types
Three or More Samples with Full Nitrogen Series

## Slide 15
Single Family all Types by System Type
Three or More Samples with Full Nitrogen Series
System Type | Total with 3+ Samples | Total below 19mg/l | Mashpee Percentage | County Percentage
All Types | 89 | 58 | 65% | 75%
Advantex | 12 | 10 | 83% | 81%
Bioclere | 7 | 5 | 71% | 74%
FAST | 40 | 28 | 70% | 80%
Septitech | 16 | 6 | 38% | 58%
Singulair | 4 | 4 | 100% | 90%
Waterloo | 6 | 6 | 100% | 73%
Clivus | 1 | 1 | 100% | -
RSF | 1 | 0 | 0% | 54%

## Slide 16: Multi-Family all Types by Individual System
Three or More Samples with Full Nitrogen Series

## Slide 17: Commercial all Types by Individual System
Three or More Samples with Full Nitrogen Series

## Slide 18
Keeping Track of it All…
The I/A Tracking Database
The program so far:
1,630 individual systems.
34 different I/A technologies.
Over 13,400 sample reports filed.
Over 100,000 individual water quality data points.
On-line data access:
  http://www.barnstablecountyhealth.org/ia-systems/information-center/data-and-statistics/ia-box-whisker-diagrams
In the future:
50+ new systems added each year in recent years.
1400+ sample reports submitted each year.
10,000+ water quality data points each year.
Expanding out to other towns.
New tracking database to take program to the next level and enable enhanced tracking of an increased load of I/A systems.

## Slide 19: Taking The Next Step
Develop new tracking database with enhanced I/A compliance tracking capabilities.
Increase homeowner and system operator accountability.
Disperse more information to the public and public officials for decision making.
Expand the program to include non-I/A systems.

## Slide 20: Focus on Accountability
Homeowners, designers, installers, maintenance providers held more accountable for system performance.
Example – when system operator enters a sample report which contains a sample parameter exceedance (i.e. total nitrogen over 19 mg/l), homeowner and BOH are notified and operator receives instantaneous feedback about what the town-required follow-up is.

## Slide 21: Better Information for Informed Wastewater Decisions
Making analyzed sample and inspection data more accessible to both town officials and citizens.
Real-world system performance data for total nitrogen, phosphorus, etc.
Real-world data on persistent maintenance issues. Ex – repeated recirculation pump failures leading to higher TN concentration in effluent.
Access to better data helps BOH make decisions which work toward nutrient loading targets.

## Slide 22: Expand Beyond I/A
Develop database to track all on-site septic systems.
Enable tracking of septic system components not considered I/A.
Analyze failure rates to identify specific types of components which may need review. Example – a particular type of polyethylene tank that fails much quicker than expected.
Have an inventory of all systems and their components in town (over time).

## Slide 23: Innovative/Alternative Septic System Performance
Brian Baumgaertel
508-375-6888
bbaumgaertel@barnstablecounty.org
Barnstable County Department of Health and Environment